## Slide 1: Dynamics

## Slide 2: Mathematical notation
Consists of Body, Thigh, Shank
Angles measured relative to previous link
Leg 1 – Front Right
Leg 2 – Rear Right
Leg 3 – Front Left
Leg 4 – Rear Left
X
Y
Θ thigh
Θ body
Θ shank
Leg 1
Leg 2
Leg 3
Leg 4
Thigh
Shank

## Slide 3: Non-Inertial Reference frames
Due to robot acceleration the system is non-inertial
Two solutions:
  Euler-Newton, F=ma with an arbitrary ground point or virtual inertial forces
  Lagrange-Euler, energy approach with generalized coordinate systems
Euler-Newton was selected with an arbitrary ground point off the robot chassis due to its familiarity
Torque equations modified with equivalent torques

## Slide 4: Free Body Diagrams
Used to find joint reaction forces and torques required for motion
Torque equations summed about origin
Solution assumes knowledge of kinematic state and foot forces

## Slide 5: Kinematics
Four 2R serial linkage originating at the body’s center of gravity
Body CG is at point (x, y)
16 equations to define link positions in x and y

## Slide 6: Jacobian differentiation
Simplification of the Full Derivative of a multivariable function
Used to calculate velocity and acceleration of links
Break function derivative into a Jacobian and time derivative vector
Allows symbolic equation solution with MATLAB for faster iteration
Hand verified
=

## Slide 7: State Vector
Jacobian differentiation is used to calculate the velocity and acceleration of each joint
Positions, velocities, and accelerations are all in terms of a state vector, q
Joint torques and forces are also functions of q

## Slide 8: Step simulation
Kinematic simulation used to calculate joint position, velocity, and acceleration during motion
Takes foot path, step time, and dt as inputs
Outputs full joint state every time step

## Slide 9: Foot force derivation
Final unknowns for torque and force calculations are the foot forces
Step split into three phases
  Drag phase – Foot is pulling robot chassis while in no-slip ground contact
  Swing phase – Foot is swinging through the air
  Impulse phase – Foot impacts ground at the furthest forward position

## Slide 10: Foot Force Derivation - Drag
Calculated using FBD of full robot
  Assuming some constant forward velocity
  Assuming no slip between pulling foot and ground
  Coefficient of friction 0.5
  Robot weight split evenly between legs
X
Y
w
FF2Y
FF3Y
FF4Y
FF1X
FF3X
FF3X
FF3X
FF1Y

## Slide 11: Foot Force Derivation - Swing
X
Y
Calculated using FBD of full robot
  No forces acting on swinging foot
  Weight evenly distributed on other feet
  X direction foot forces approximately zero
w
FF2Y
FF3Y
FF4Y

## Slide 12: Foot Force Derivation - Impulse
X
Y
Calculated using impulse and conservation of momentum on foot
  Assuming impulse force is constant
  Assuming other leg forces are same as the swing phase
w
FF2Y
FF1Y
FF4Y
FF3Y
FF1X

## Slide 13: Results
Torques and forces used for finite element analysis of structural elements
Torques used with motion study to determine cylinder stroke, bore size, and maximum pressure
Cylinder analysis used to create specifications for other pneumatic components, such as storage tanks and tubing/valve size