## Slide 1: Team Agile Robotic Control
Logan Beaver
Justin Campbell
Tyler Paddock
Ronald Shipman

## Slide 2: Project Overview
Develop initial robotics platform
Public Outreach
  Increase interest in STEM fields
  Engineering deficit
  Fluid Power
Educational robotics platform
  Fluid Power
  Control Systems
  Robotics

## Slide 3: Major Design Decisions
Quadruped Locomotion
  Agile motion
  Stable
  Rugged Terrain
Pneumatic Power
  High energy density
  Clean and lightweight

## Slide 4: Mechanical Design

## Slide 5: Power Source Options
 | Advantages | Disadvantages
Hydraulic Power Source | -Highest achievable power density | -High maintenance -Heavy -Dirty
Electric Power Source | -Accurate positioning | -Lowest achievable power density -Noncompliant
Pneumatic Power Source | -Higher power density than electric power -Low Maintenance -Compliant action from fluid compression | -Compressible fluid causes inaccuracy in positioning

## Slide 6: Components
Pneumatic components include:
Receiver Tank
Air Compressor
Double Acting Air Cylinders (w/ feedback)
Solenoid Valve
Directional Control Valves (4/2)
Pressure Relief Valve
Tubing

## Slide 7: Pneumatic Circuit

## Slide 8: Kinematic Modelling
Homogenous Transformations
Determines cylinder stroke

## Slide 9: Dynamic Model
Lagrangian Mechanics
Non-inertial reference frames
Arbitrary global reference frame
Determines mechanical properties of components
27 Equations

## Slide 10: Control architecture
Control algorithms: Software implemented PIDs
Software: MATLAB/Simulink and associated CODER software
Simulink model of the control is developed and then C code is generated for the target hardware
Current hardware is an Arduino Mega 2560
The feedback in the control loop will be a position feedback from the cylinder

## Slide 11
<Picture of Simulink model with PIDs>

## Slide 12: Signal Conditioning
PWM signals from the microcontroller are filtered into analog signals to drive the pneumatic actuators
The analog signals will be scaled by amplifiers to the correct voltage required by the pneumatic actuator
Opto-isolators used to protect microcontroller by separating power circuits

## Slide 13: User Interface and Remote COntrol
Xbee short range radio devices using IEEE standard 802.15.4
Range: 100 meters
250Kbps maximum
2.4GHz operating frequency

## Slide 14: What’s Next?
Determine necessary output forces of cylinders based on kinematic equations
Select appropriate pneumatic components based on needed specifications
Test air cylinders
Pneumatic circuit construction
Test circuit with control system

## Slide 15: Questions?