## Slide 1: agile and educational robotics platform
Team A.R.C.
Logan Beaver
Justin Campbell
Tyler Paddock
Ron Shipman

## Slide 2: Project Overview
Develop initial robotics platform
Public Outreach
  Increase interest in STEM fields – 15% decrease in STEM interest in 2013
  Low math and science proficiency – 65th percentile math, 50th percentile science
  Fluid Power
Educational robotics platform
  Fluid Power
  Control Systems
  Robotics

## Slide 3: Major Design Decisions
Quadruped Locomotion
  Agile motion
  Stable
  Rugged Terrain
  Two Links per Leg
Pneumatic Power
  High energy density
  Clean and lightweight

## Slide 4: Major Constraints and Objectives
Does not weight over 35 Kg
Operational speed up to 0.5 m/s
Gait implementations for creep and walk
Emergency stops easily accessible
Battery life of at least 3 hours for pneumatic components
Onboard batteries and control system
Tethered air supply

## Slide 5: Dynamics And Simulations
Mathematical Notation
Free Body Diagrams
Kinematic Modelling
Dynamic Simulation
Foot force calculation

## Slide 6: Mathematical notation
Consists of Body, Thigh, Shank
Angles measured relative to previous link
Leg 1 – Front Right
Leg 2 – Rear Right
Leg 3 – Front Left
Leg 4 – Rear Left
X
Y
Θ thigh
Θ body
Θ shank
Leg 1
Leg 2
Leg 3
Leg 4
Thigh
Shank

## Slide 7: Non-Inertial Reference frames
Due to robot’s acceleration the system is not in an inertial reference frame
Two solutions:
  Euler-Newton: F=ma with an arbitrary ground point or virtual inertial forces
  Lagrange-Euler: energy approach with generalized coordinate systems
Euler-Newton was selected due to its familiarity
  arbitrary ground point off the robot chassis
Torque equations modified with equivalent torques to compensate

## Slide 8: Free Body Diagrams
Used to find joint reaction forces and torques required for motion
Torque equations summed about origin
Solution assumes knowledge of kinematic state and foot forces

## Slide 9: Kinematics
Four three-bar serial linkages originating at the body’s center of gravity
Body CG is at point (x, y)
16 equations to define link positions

## Slide 10: Jacobian differentiation
Simplification of the Full Derivative of a multivariable function
Used to calculate velocity and acceleration of links
Break function derivative into a Jacobian and time derivative vector
Allows symbolic equation solution with MATLAB for faster iteration
Verified with hand calculations
=

## Slide 11: State Vector
Positions, velocities, and accelerations are all in terms of a state vector, q
By extension, joint torques and forces are functions of q

## Slide 12: Step simulation
Kinematic simulation used to calculate joint position, velocity, and acceleration during motion
Takes foot path, step time, and dt as inputs
Outputs full joint state every time step

## Slide 13: Foot force derivation
Final unknowns for torque and force calculations are the foot forces
Step split into three phases
  Drag phase – Foot is pulling robot chassis while in no-slip ground contact
  Swing phase – Foot is swinging through the air
  Impulse phase – Foot impacts ground at the furthest forward position

## Slide 14: Foot Force Derivation - Drag
Calculated using FBD of full robot
  Assuming some constant forward velocity
  Assuming no slip between pulling foot and ground
  Coefficient of friction 0.5
  Robot weight split evenly between legs
X
Y
w
FF2Y
FF3Y
FF4Y
FF1X
FF3X
FF3X
FF3X
FF1Y

## Slide 15: Foot Force Derivation - Swing
X
Y
Calculated using FBD of full robot
  No forces acting on swinging foot
  Weight evenly distributed on other feet
  X direction foot forces approximately zero
w
FF2Y
FF3Y
FF4Y

## Slide 16: Foot Force Derivation - Impulse
X
Y
Calculated using conservation of momentum on leg
  Assuming impulse force is constant
  Assuming other leg forces are unchanged from the swing phase
w
FF2Y
FF1Y
FF4Y
FF3Y
FF1X

## Slide 17: Results
Torques and forces used for finite element analysis of structural elements
Torques used with motion study to determine cylinder stroke, bore size, and maximum pressure
Cylinder analysis used to create specifications for other pneumatic components, such as storage tanks and tubing/valve size

## Slide 18: Mechanical Design
Component Design
  Chassis
  Thigh/shank
Material Choices
FEA of Components

## Slide 19: Chassis
Main support for the body
Houses all electric and pneumatic components
  Needs to allow easy access to components
  Provide protection from falls/collisions
Lightweight design to reduce the overall forces on the legs

## Slide 20: Thigh/Shank
Based on the leg structure of quadruped mammals
  Removal of 3rd joint for simplification of design
  Bent thigh to compensate for lost mobility
  Prevents singularity point of knee piston
Step length used to determine component lengths

## Slide 21: Material Choices
Chassis
  6105-T5 T-Slotted Aluminum framing
  Strong, lightweight material
  Number of plates/brackets available for easy assembly
Thigh/Shank
  6061 Aluminum
  Good strength, machinability, and easily welded

## Slide 22: Finite Element Analysis of Components

## Slide 23: Pneumatics
Benefits of pneumatics over other power sources
Component Specifications
  Air Cylinders
  Directional Control Valves
  Air Compressors
Other circuit components

## Slide 24: Power Source Options
 | Advantages | Disadvantages
Hydraulic Power Source | -Highest achievable power density | -High maintenance -Heavy -Dirty
Electric Power Source | -Accurate positioning | -Lowest achievable power density -Noncompliant
Pneumatic Power Source | -Higher power density than electric power -Low Maintenance -Compliant action from fluid compression | -Compressible fluid causes inaccuracy in positioning

## Slide 25: Air Cylinders
Converts fluid power into mechanical power
Position Feedback Sensor
Specifications limited by:
-Volume available for cylinder placement
-Necessary pressure
-Necessary volumetric flow rate

## Slide 26: Example Specification process
Extend phase:
Retract Phase:
Total Volumetric Flow:
at STP
Selected Cylinder Specs:
2 inch Bore Diameter
4 inch Stroke Length
Required Cylinder Specs:
178 lbf max output
4 inch stroke length
60 cycles per minute

## Slide 27: Directional Control Valves (DCV)
Controls fluid flow through air cylinders based on spool position
Specifications determined by:
-Necessary volumetric flow rate to air cylinder
4-3 DCV

## Slide 28: Air Compressor
Compresses air absorbed from
surrounding environment
Feeds to components downstream
Specifications limited by:
-Maximum Pressure required by air cylinders
-Average volumetric flow rate required by air cylinders

## Slide 29
Remaining Pneumatic components include:
Receiver Tank
-Sized depending on additional flow needs
Solenoid Valve
-Main on/off switch of fluid flow to system
Pressure Relief Valve
-Dictates upper pressure limit
Tubing

## Slide 30: Chosen Specifications
Air Cylinders (8): 2 inch bore diameter, 3 inch stroke length for shank, 4 inch stroke length for thigh
Directional Control Valves (8): 5 ports, 3 spool positions, Cv = 0.67 (21 CFM)
Air Compressor: 10 gallon, 5.3 CFM (At 90 psi), 125 psi maximum pressure

## Slide 31: Pneumatic Circuit Segment

## Slide 32: Electrical
Microcontroller and Programming
Control Algorithms
Communication System
Debug Panel
Control Signal and Feedback Conditioning

## Slide 33: Microcontroller and Programming
Arduino Mega 2560 is used to control the system’s actions
Advantages
-Low cost microcontroller
-Analog inputs
-Pulse-width modulated outputs
Mathwork’s Simulink models cross compiled to microcontroller

## Slide 34: Control Algorithms
The Simulink PID algorithms are used for control
Implementation of a step is done using state machine architecture
The state machine drives the PID in each control loop

## Slide 35: Control Algorithm For One Leg

## Slide 36: Communication System
XBee Series 1 Radio
  -IEEE 802.15.4 protocol
  -Operational Frequency 2.4 GHz
Mounted onto the Arduino through XBee Shield
User interface runs on PC Simulink model

## Slide 37: Debug Panel
Standard for MSOE test equipment – Banana Plug
On Switch
Emergency Stop – Cuts Power to valve solenoids
Battery Level Indicators
Status LEDs

## Slide 38: Debug Panel – 9 volt battery Indicator
Three LEDs in series with zener diodes
LED colors: Green, Yellow, Red

## Slide 39: Debug Panel Diagram
<Diagram to be added here>

## Slide 40: Control Signal and Feedback Conditioning
Signal Conditioning
PWM -> analog voltage -> optical signal -> analog voltage
Opto-isolator separates electrical circuits

## Slide 41: Questions?