## Slide 1: Team Agile Robotic Control
Logan Beaver - ME
Justin Campbell - ME
Tyler Paddock – CE
Ronald Shipman – ME
Dr. Luis Rodriguez – advisor

## Slide 2: Project Overview
Develop initial robotics platform
Public Outreach
  Increase interest in STEM fields
  Engineering deficit
  Fluid Power
Educational robotics platform
  Fluid Power
  Control Systems
  Robotics
Iterated by future teams

## Slide 3: Major Design Decisions
Quadruped Locomotion
  Agile motion
  Dynamically stable
  Rugged terrain capability
Pneumatic Actuators
  High energy density
  Clean and lightweight
  Compliant action

## Slide 4: Major Constraints and Objectives
Maximum weight of 35 kg
Top speed of 0.5 m/s
Implementation of drag gait
Easily accessible emergency stops
3 Hour Battery Life
Onboard batteries and control systems
Tethered air supply with additional onboard storage space

## Slide 5: Simulation and design
Derived from initial kinematic equations
Put in state matrix form
Kinematic simulation used to get robot state at different positions
Required forces and torques determined from robot state

## Slide 6: Simulation and design
Dynamic simulations were used to design the initial robot
Torque analysis for pneumatic actuator design
Force analysis for mechanical design
Kinematic simulation for control system design

## Slide 7: Pneumatic design
Eight two directional air cylinders, two for each leg
Eight 4/3 solenoid directional control valves
Soft start/dump solenoid valve
Controlled with Arduino Mega microcontroller running Simulink

## Slide 8: Pneumatic Circuit

## Slide 9: Pneumatic Construction

## Slide 10: Mechanical system
Chassis constructed from 20mm, 80/20 extruded aluminum
Aluminum plate added to bottom to allow for component placement
Legs are made out of 6061-T5 Aluminum
Bearings placed at each hip and knee joints to improve motion

## Slide 11: Current Chassis Construction

## Slide 12: Current Leg Construction
Add full leg picture

## Slide 13: Electrical design
DC valves require 24v power and two 10v command signals
Amplifier requires + and – negative rails to perform signal conditioning
Switch Capacitor Voltage Converter circuit provides negative rail
Cylinder Position Feedback is a Linear Resistive Transducer
9v power supply to Arduino Mega and 30 volt supply for the valves
Debug panel
  Battery indicator LEDs
  Banana plugs for compatibility with MSOE lab equipment
  Emergency Stop

## Slide 14: Arduino Mega PWM to Analog
Third Order Sallen-Key Low Pass Filter

## Slide 15: Filter Response
Higher order filter was used to get a smooth response
Third order filter was selected to maintain fabrication simplicity

## Slide 16: Debug Panel Layout
USB Plug: Program with disassembly
Emergency Stop: Removes valve power
Banana Connections: Each leg’s control signal is accessible
Comms. Status LED: Indicate communication system connection
Status LED: Indicate status states in the software

## Slide 17: Switched Capacitor Voltage Converter
Notice the breadboard style PCB board
Disadvantages:
Soldering the connections
Not as clean as a custom PCB board
Advantages:
Modifications are possible for future teams
More secure than breadboard prototyping
Low cost (several dollars per board) vs, custom design runs

## Slide 18: Control scheme
Code generated from Simulink model
Uses a Stateflow diagram to control foot position based on user input
User controls microcontroller via joystick with a custom java HMI through a wireless zigbee communicator
Currently uses a lookup table with index to determine next foot position
Delays next command until position is within a threshold of desired

## Slide 19: Control scheme – Single Leg

## Slide 20: Simulink PID Model

## Slide 21: Stateflow Diagram
Takes in (-1, 0, 1) as user commands
Adjusts lookup table index
Eventually used to handle disturbance response and turning

## Slide 22: Following a series of step inputs

## Slide 23: What’s Next?
Finish robot leg assembly
Integrate pneumatic components with robot chassis
Configure control scheme to consider a full leg
Frequency response of pneumatics to determine plant transfer function
Create final motherboard circuit
Finish debug panel construction
Implement drag gait
Ensure documentation is clear and complete for next year’s groups

## Slide 24: Questions?