## Slide 1: Team Agile Robotic Control
Logan Beaver - ME
Justin Campbell - ME
Tyler Paddock – CE/EE
Ronald Shipman – ME
Dr. Luis Rodriguez – advisor

## Slide 2: Project Overview
Develop initial robotics platform
Public Outreach
  Increase interest in STEM fields
  Engineering deficit
  Fluid Power
Educational robotics platform
  Fluid Power
  Control Systems
  Robotics

## Slide 3: Major Design Decisions
Quadruped Locomotion
  Agile motion
  Stable
  Rugged Terrain
  Two Links per Leg
Pneumatic Power
  High energy density
  Clean and lightweight

## Slide 4: Major Constraints and Objectives
Does not weight over 35 Kg
Operational speed up to 0.5 m/s
Gait implementations for creep and walk
Emergency stops easily accessible
Battery life of at least 3 hours for pneumatic components
Onboard batteries and control system
Tethered air supply

## Slide 5: Power Source Options
 | Advantages | Disadvantages
Hydraulic Power Source | -Highest achievable power density | -High maintenance -Heavy -Dirty
Electric Power Source | -Accurate positioning | -Lowest achievable power density -Noncompliant
Pneumatic Power Source | -Higher power density than electric power -Low Maintenance -Compliant action from fluid compression | -Compressible fluid causes inaccuracy in positioning

## Slide 6: Components
Pneumatic components include:
Receiver Tank
Air Compressor
Double Acting Air Cylinders (w/ feedback)
Solenoid Valve
Directional Control Valves (4/2)
Pressure Relief Valve
Tubing

## Slide 7: Pneumatic Circuit for single cylinder

## Slide 8: Design Ideas
Arachnea
Hexabot
Boxxy
DogeBot

## Slide 9: Mechanical Design Matrix

## Slide 10: Dogebot
Pros
  Legs cannot interfere with each other
  Adequate space for components
  Open sides for easy accessibility
Cons
  Legs may be susceptible to bending
  Near the limit on all dimensions and weight

## Slide 11: Design Updates
Chassis
  Extruded T-Slotted Aluminum Frame
  Easy to assemble and attach components
  Decreased dimensions to reduce weight
Legs
  Fixed piston attachment points
  Attached to top of chassis to increase stability

## Slide 12: DogeBot 2.0

## Slide 13
Kinematic Model
Homogenous Transformations
Determines cylinder stroke
Shank X Acceleration:

## Slide 14
Dynamic Model
Non-inertial reference frame
Lagrangian Mechanics
Arbitrary global reference frame
Determines mechanical properties of components
27 Equations with state vector q

## Slide 15: Control architecture
Control algorithms: Software implemented PIDs
Software: MATLAB/Simulink model of the control is developed and
Hardware: Arduino Mega 2560
Control Feedback: Position feedback from the pneumatic cylinders

## Slide 16: PID Model

## Slide 17: Signal Conditioning
PWM signals from the microcontroller are filtered into analog signals to drive the pneumatic actuators
The analog signals will be scaled by amplifiers to the correct voltage required by the pneumatic actuator
Opto-isolators used to protect microcontroller by separating power circuits

## Slide 18: User Interface and Remote COntrol
Xbee short range radio devices using IEEE standard 802.15.4
Range: 100 meters
250Kbps maximum
2.4GHz operating frequency

## Slide 19: What’s Next?
Decide on final pneumatic cylinder based on simulations
Operational Motherboard Assembled
Gather air cylinder response data
Experiment with single pneumatic leg control
Build and assemble robot subsystems
Observe final system behavior
Test gait implementations

## Slide 20: Questions?