## Slide 1
Design Constraints/Criteria
A maximum weight of 35 kg for portability
Maximum size of 0.75 m x 0.75 m x 1.0 m box for portability
Custom debug panel creation to facilitate troubleshooting
MATLAB and Simulink model support to allow mechanical engineering students to update control algorithms without knowledge of C/C++
Electronic fuses and shielding to protect the robot and operator during use and maintenance
Mechanical protection to reduce the risk of pinching and self-collision damage to the robot
An easy to access emergency stop to quickly depower the robot
A pressure relief valve to reduce the risk of overloading and damaging pneumatic components
Problem Statement
Milwaukee School of Engineering (MSOE) participates in community outreach programs where science, technology, engineering, and mathematics (STEM) topics are demonstrated to encourage younger generations to enter into STEM based degrees and careers. Having an automated control system to demonstrate and interact with would increase the excitement at these outreach programs. Development of a robot with pneumatic locomotion for the Milwaukee School of Engineering’s controls classes would give students a first-hand experience with complex control systems.
Mechanical Design
Chassis Construction
6105-T5 T-Slotted Aluminum Framing (Yield Strength = 275 Mpa)
6061 Aluminum Plate (Yield Strength = 276 Mpa)
Leg Construction
6061 Aluminum Bar (Yield Strength = 276 Mpa)
Pneumatic Design
Using pneumatic systems as the driving force for the legs, the following components will be utilized:
Double-acting, air cylinders with position feedback sensors (1.5 in. bore diameter)
Two-solenoid 4 way 3 position directional control valves (0.37 Cv)
Air-compressor
Pressure relief valve
Soft start/dump solenoid valve
Secondary receiver tank
Inverse Leg Kinematics
Forward Leg Kinematics
Angle to Cylinder Length
Cylinder Length to Angle
Desired Foot Position
Set by State Machine
Control System
Development of an Agile Educational Robot
Team A.R.C.
Logan Beaver
Justin Campbell
Tyler Paddock
Ronald Shipman
Spring, 2015
Acknowledgements
Special thanks to Joy Global, Inc., the National Fluid Power Association, Emerson and Dr. Luis A. Rodriguez for their support
Electrical Design