## Slide 1: agile and educational robotics platform
Team A.R.C.
Logan Beaver
Justin Campbell
Tyler Paddock
Ron SHipman

## Slide 2: Introduction

## Slide 3: Dynamics And Simulations

## Slide 4: Mathematical notation
Consists of Body, Thigh, Shank
Angles measured relative to previous link
Leg 1 – Front Right
Leg 2 – Rear Right
Leg 3 – Front Left
Leg 4 – Rear Left
X
Y
Θ thigh
Θ body
Θ shank
Leg 1
Leg 2
Leg 3
Leg 4
Thigh
Shank

## Slide 5: Non-Inertial Reference frames
Due to robot acceleration the system is non-inertial
Two solutions:
  Euler-Newton, F=ma with an arbitrary ground point or virtual inertial forces
  Lagrange-Euler, energy approach with generalized coordinate systems
Euler-Newton was selected with an arbitrary ground point off the robot chassis due to its familiarity
Torque equations modified with equivalent torques

## Slide 6: Free Body Diagrams
Used to find joint reaction forces and torques required for motion
Torque equations summed about origin
Solution assumes knowledge of kinematic state and foot forces

## Slide 7: Kinematics
Four three-bar serial linkages originating at the body’s center of gravity
Body CG is at point (x, y)
16 equations to define link positions

## Slide 8: Jacobian differentiation
Simplification of the Full Derivative of a multivariable function
Used to calculate velocity and acceleration of links
Break function derivative into a Jacobian and time derivative vector
Allows symbolic equation solution with MATLAB for faster iteration
Hand verified
=

## Slide 9: State Vector
Jacobian differentiation is used to calculate the velocity and acceleration of each joint
Positions, velocities, and accelerations are all in terms of a state vector, q
By extension, joint torques and forces are functions of q

## Slide 10: Step simulation
Kinematic simulation used to calculate joint position, velocity, and acceleration during motion
Takes foot path, step time, and dt as inputs
Outputs full joint state every time step

## Slide 11: Foot force derivation
Final unknowns for torque and force calculations are the foot forces
Step split into three phases
  Drag phase – Foot is pulling robot chassis while in no-slip ground contact
  Swing phase – Foot is swinging through the air
  Impulse phase – Foot impacts ground at the furthest forward position

## Slide 12: Foot Force Derivation - Drag
Calculated using FBD of full robot
  Assuming some constant forward velocity
  Assuming no slip between pulling foot and ground
  Coefficient of friction 0.5
  Robot weight split evenly between legs
X
Y
w
FF2Y
FF3Y
FF4Y
FF1X
FF3X
FF3X
FF3X
FF1Y

## Slide 13: Foot Force Derivation - Swing
X
Y
Calculated using FBD of full robot
  No forces acting on swinging foot
  Weight evenly distributed on other feet
  X direction foot forces approximately zero
w
FF2Y
FF3Y
FF4Y

## Slide 14: Foot Force Derivation - Impulse
X
Y
Calculated using impulse and conservation of momentum on leg
  Assuming impulse force is constant
  Assuming other leg forces are unchanged from the swing phase
w
FF2Y
FF1Y
FF4Y
FF3Y
FF1X

## Slide 15: Results
Torques and forces used for finite element analysis of structural elements
Torques used with motion study to determine cylinder stroke, bore size, and maximum pressure
Cylinder analysis used to create specifications for other pneumatic components, such as storage tanks and tubing/valve size

## Slide 16: Mechanical

## Slide 17: Pneumatics
Benefits of pneumatics over other power sources
Component Specifications
  Air Cylinders
  Directional Control Valves
  Air Compressors
Other circuit components

## Slide 18: Power Source Options
 | Advantages | Disadvantages
Hydraulic Power Source | -Highest achievable power density | -High maintenance -Heavy -Dirty
Electric Power Source | -Accurate positioning | -Lowest achievable power density -Noncompliant
Pneumatic Power Source | -Higher power density than electric power -Low Maintenance -Compliant action from fluid compression | -Compressible fluid causes inaccuracy in positioning

## Slide 19: Air Cylinders
Converts fluid power into mechanical power
Position Feedback Sensor
Specifications determined by:
-Appropriate bore diameter
-Appropriate necessary pressure
-Appropriate necessary volumetric flow rate

## Slide 20: Example Specification
Extend phase:
Retract Phase:
Total Volumetric Flow:
Selcted Cylinder Specs:
2 inch Bore Diameter
4 inch Stroke Length
Required Cylinder Specs:
178 lbf max output
4 inch stroke length
60 cycles per minute

## Slide 21: Directional Control Valves
Controls fluid flow through air cylinders based on spool position
Specifications determined by:
-Necessary volumetric flow rate to air cylinder
4-3 DCV

## Slide 22: Air Compressor
Compresses air absorbed from
surrounding environment
Feeds to components downstream
Specifications determined by:
-Maximum Pressure required by air cylinders
-Average volumetric flow rate required by air cylinders

## Slide 23
Remaining Pneumatic components include:
Receiver Tank
Solenoid Valve
Pressure Relief Valve
Tubing

## Slide 24: Chosen Specifications
Air Cylinders (8):
Directional Control Valves (8):
Air Compressor:

## Slide 25: Pneumatic Circuit

## Slide 26: Electrical
Microcontroller and Programming
Control Algorithms
Communication System
Debug Panel
Control Signal and Feedback Conditioning

## Slide 27: Microcontroller and Programming
Arduino Mega 2560 is used to control the system’s actions
Advantages
-Low cost microcontroller
-Analog inputs
-Pulse-width modulated outputs
Mathwork’s Simulink models cross compiled to microcontroller

## Slide 28: Control Algorithms
The Simulink PID algorithms are used for control
Implementation of a step is done using state machine architecture
The state machine drives the PID in each control loop

## Slide 29: Control Algorithm For One LEg

## Slide 30: Communication System
XBee Series 1 Radio
  -IEEE 802.15.4 protocol
  -Operational Frequency 2.4 GHz
Mounted onto the Arduino through XBee Shield
User interface runs on PC Simulink model

## Slide 31: Debug Panel
Standard for MSOE test equipment – Banana Plug
On Switch
Emergency Stop – Cuts Power to valve solenoids
Battery Level Indicators
Status LEDs

## Slide 32: Debug Panel – 9 volt battery Indicator
Three LEDs in series with zener diodes
LED colors: Green, Yellow, Red

## Slide 33: Debug Panel Diagram
<Diagram to be added here>

## Slide 34: Control Signal and Feedback Conditioning
Signal Conditioning
PWM -> analog voltage -> optical signal -> analog voltage
Opto-isolator separates electrical circuits

## Slide 35: Questions?