## Slide 1: Team Agile Robotic Control
Logan Beaver
Justin Campbell
Tyler Paddock
Ronald Shipman

## Slide 2: Project Overview
Develop initial robotics platform
Public Outreach
  Increase interest in STEM fields
  Engineering deficit
  Fluid Power
Educational robotics platform
  Fluid Power
  Control Systems
  Robotics

## Slide 3: Major Design Decisions
Quadruped Locomotion
  Agile motion
  Stable
  Rugged Terrain
Pneumatic Power
  High energy density
  Clean and lightweight

## Slide 4: Mechanical Design

## Slide 5: Power Source Options
 | Advantages | Disadvantages
Hydraulic Power Source | -Highest achievable power density | -High maintenance -Heavy -Dirty
Electric Power Source | -Accurate positioning | -Lowest achievable power density -Noncompliant
Pneumatic Power Source | -Higher power density than electric power -Low Maintenance -Compliant action from fluid compression | -Compressible fluid causes inaccuracy in positioning

## Slide 6: Components
Pneumatic components include:
Air Supply Tank
Air Compressor
Double Acting Air Cylinders (w/ feedback)
Receiver Tank
Solenoid Valve
Directional Control Valves (4/2)
Pressure Relief Valve
Tubing

## Slide 7: Pneumatic Circuit

## Slide 8: Kinematic Modelling
Homogenous Transformations
Determines cylinder stroke

## Slide 9: Dynamic Model
Lagrangian Mechanics
Non-inertial reference frames
Arbitrary global reference frame
Determines mechanical properties of components
27 Equations

## Slide 10: Control architecture
Control algorithms (PIDs) implemented in software
Software used in this project is MATLAB, Simulink, and the associated CODER software
Simulink model of the control is developed and then C code is generated for the target hardware.
Current hardware is an Arduino Mega 2560

## Slide 11
<Picture of Simulink model with PIDs>

## Slide 12: Signal Conditioning
To drive the pneumatic actuators digital PWM signals from the microcontroller will be filtered by a low pass filter into analog signals
The analog signals will be scaled by amplifiers to the correct voltage required by the pneumatic actuator
Circuit isolation is needed to separate the 5 volt microcontroller circuit from the 12 volt actuator circuit
Circuit isolation will be achieved using opto-isolators
The feedback in the control loop will be a position feedback from the cylinder

## Slide 13: User Interface
The robot will be remotely controlled by a human operator
Xbee short range radio devices using IEEE standard 802.15.4 will be used to handle the wireless communication
<Picture of controller, Xbee device, transmission medium, radio waves>

## Slide 14: What’s Next?
Determine necessary output forces of cylinders based on kinematic equations
Select appropriate pneumatic components based on needed specifications
Test air cylinders
Pneumatic circuit construction
Test circuit with control system

## Slide 15: Questions?