## Slide 1: Team Agile Robotic Control
Logan Beaver
Justin Campbell
Tyler Paddock
Ronald Shipman

## Slide 2: Project Overview
Develop initial robotics platform
Public Outreach
  Increase interest in STEM fields
  Engineering deficit
  Fluid Power
Educational robotics platform
  Fluid Power
  Control Systems
  Robotics

## Slide 3: Major Design Decisions
Quadruped Locomotion
  Agile motion
  Stable
  Rugged Terrain
Pneumatic Power
  High energy density
  Clean and lightweight

## Slide 4: Design Ideas
Arachnea
Hexabot
Boxxy
DogeBot

## Slide 5: Mechanical Design Matrix

## Slide 6: Dogebot
Pros
  Legs cannot interfere with each other
  Adequate space for components
  Open sides for easy accessibility
Cons
  Legs may be susceptible to bending
  Near the limit on all dimensions and weight

## Slide 7: Design Updates
Chassis
  Extruded T-Slotted Aluminum Frame
  Easy to assemble and attach components
  Decreased dimensions to reduce weight
Legs
  Fixed piston attachment points
  Attached to top of chassis to increase stability

## Slide 8: DogeBot 2.0

## Slide 9: Power Source Options
 | Advantages | Disadvantages
Hydraulic Power Source | -Highest achievable power density | -High maintenance -Heavy -Dirty
Electric Power Source | -Accurate positioning | -Lowest achievable power density -Noncompliant
Pneumatic Power Source | -Higher power density than electric power -Low Maintenance -Compliant action from fluid compression | -Compressible fluid causes inaccuracy in positioning

## Slide 10: Components
Pneumatic components include:
Receiver Tank
Air Compressor
Double Acting Air Cylinders (w/ feedback)
Solenoid Valve
Directional Control Valves (4/2)
Pressure Relief Valve
Tubing

## Slide 11: Pneumatic Circuit

## Slide 12: Kinematic Modelling
Homogenous Transformations
Determines cylinder stroke

## Slide 13: Dynamic Model
Lagrangian Mechanics
Non-inertial reference frames
Arbitrary global reference frame
Determines mechanical properties of components
27 Equations

## Slide 14: Control architecture
Control algorithms: Software implemented PIDs
Software: MATLAB/Simulink and associated CODER software
Simulink model of the control is developed and then C code is generated for the target hardware
Current hardware is an Arduino Mega 2560
The feedback in the control loop will be a position feedback from the cylinder

## Slide 15
<Picture of Simulink model with PIDs>

## Slide 16: Signal Conditioning
PWM signals from the microcontroller are filtered into analog signals to drive the pneumatic actuators
The analog signals will be scaled by amplifiers to the correct voltage required by the pneumatic actuator
Opto-isolators used to protect microcontroller by separating power circuits

## Slide 17: User Interface and Remote COntrol
Xbee short range radio devices using IEEE standard 802.15.4
Range: 100 meters
250Kbps maximum
2.4GHz operating frequency

## Slide 18: What’s Next?
Determine necessary output forces of cylinders based on kinematic equations
Select appropriate pneumatic components based on needed specifications
Test air cylinders
Pneumatic circuit construction
Test circuit with control system

## Slide 19: Questions?